## Slide 1: GTU CSE496 ECG Classification Using Transformer Networks
CSE496
Second Presentation
Emre Güven
Project Advisor: Prof. Dr. Yusuf Sinan AKGÜL
May 2024

## Slide 2: Contents
Project Overview
Done
    Done – Data Collection
    Done – Data Cleaning and Standardization
    Done – Filtering and R-Peaks Detection
    Done – Splitting
Evaluation of Dataset Using CNN Model
Project Timeline
Success Criteria
References

## Slide 3: Project Overview
ECG signals, or electrocardiogram signals, represent the electrical activity of the heart.
Analyzing 12-channel ECG recordings with Transformer networks optimized for ECG signals to enhance diagnostic accuracy and efficiency.

## Slide 4: Done – Data Collection
Collected ECG records in 3 diagnoses from different datasets in the PhysioNet website. Diagnoses are Myocardial Infarction(MI), Hypertrophy(HYP) and Healthy Controls(NORM).
 | PTB (1000Hz, 120 secs) | PTB-XL (100Hz, 10 secs) | INCART (257Hz, 30 mins)
Healthy (NORM) | 80 | 9513 | 0
Myocardial Infarctus (MI) | 368 | 5148 | 14
Hypertrophy (HYP) | 7 | 2649 | 11

## Slide 5: Done – Data Cleaning and Standardization
PTB dataset records are split into 10-second segments.
Cleaned PTB-XL dataset with multiple diagnoses records is upsampled to 1000Hz using the Fourier method.
INCART dataset is upsampled to 1000Hz, and records are split into 10-second segments.
 | PTB |  | PTB-XL |  | INCART |  | NEW TOTAL
Healthy (NORM) | 80 | 817 | 9513 | 8577 | 0 | 0 | 9394
Myocardial Infarctus (MI) | 368 | 3550 | 5148 | 3829 | 14 | 2509 | 9888
Hypertrophy (HYP) | 7 | 73 | 2649 | 535 | 11 | 1982 | 2590

## Slide 6: Done – Filtering and R-Peaks Detection
Base-Wander filter is applied and R-peaks are detected.

## Slide 7: Done – Splitting
Splitting the long duration signals into 10-seconds segments.

## Slide 8: Evaluation of Dataset Using CNN Model
CNN Model with 5 Conv1D layers , SGD optimizer and focal loss function
PTB-XL 100Hz Combined 1000Hz

## Slide 9: Evaluation of Dataset Using CNN Model
PTB-XL 100Hz Combined 1000Hz

## Slide 10: Project Timeline

## Slide 11: Success Criteria
Preserve the integrity of the data by adjusting it appropriately when oversampling to 500Hz from sampling rates such as 100Hz and 257Hz.
Creating a dataset from various sources, which signals are adjusted to 1000Hz and 10-seconds duration.
Reach a minimum classification accuracy of 85% and an F1 score of 0.8.
Ensure that the model provides results within 10 seconds at most when given an ECG recording as input.

## Slide 12: References
Wagner, P., Strodthoff, N., Bousseljot, R., Samek, W., & Schaeffter, T. (2022). PTB-XL, a large publicly available electrocardiography dataset (version 1.0.3). PhysioNet. https://doi.org/10.13026/kfzx-aw45.
PTB Diagnostic ECG Database (Sept. 25, 2004, midnight). https://doi.org/10.13026/C28C71
St. Petersburg Institute of Cardiological Technics 12-lead Arrhythmia Database (May 1, 2008, midnight). https://doi.org/10.13026/C2V88N